## Slide 1: MinSeg Linear Dynamical Model and Feedback Control
EE 547 (PMP) Final Project
Winter 2015
Paul Adams
Chris Schulenberg

## Slide 2: MinSeg Model
Non-Linear System
State-Space Representation about equilibrium point
Arduino SoC and MinSeg sensors enable real-time measurement of state variables

## Slide 3: Stability
Transfer Function
Conclusion:
Open-loop system unstable!
Choose Pole location analysis to determine stability.

## Slide 4: Controllability
Choose Controllability Matrix analysis to determine controllability of model
Controllability matrix has full row rank
Conclusion: MinSeg is controllable

## Slide 5: Observability
Choose Observability Matrix analysis to determine observability of model
Observability matrix has full row rank
Conclusion: MinSeg is observable

## Slide 6: Controller
Choose to place the poles to provide the controller with 6 times the bandwidth of the open-loop model.
ACL = A – B*K
Conclusion: Closed-loop system is stable

## Slide 7: Estimator
Choose to place the poles to provide the observer with 6 times the bandwidth of the open-loop model.
Simulate system with observer and plot error
Conclusion: Observer tracks system states within a tight tolerance

## Slide 8: Robot/Demonstration
Challenges
  Software
  Raw sensor data
  Linking the model to the MinSeg
What worked
  Three batteries
  Reset pushbutton
  GitHub